## Slide 1: Customized ECU and Software Interface
Gang Chen

## Slide 2: Outline
Customized Nios processor for lego Car
Software Interface for Sensors
Communications between Imx6 and Nano
Demo Show

## Slide 3
Customized Nios Processor for Lego Car

## Slide 4: Hardware Features
Nios 32-bit processor (50Mhz)
32MByte SDRAM
EPCS flash
32-bit timer (used for RTOS)
Jtag-uart (for Debug)
8-Channel ADC
6 old version ultrasound IP (Not used)
8 PWM (16 channels)
4 new version ultrasound IP (used for this course)
2 encoder IP
LED, key, GPIO

## Slide 5: How to use this hardware
Download New hardware image file from the course webpage
.sof is hardware image file. Download it by using Quartus
.sopcinfo is used for BSP set-up in Nios-eclipse
.QSF indicates the pin-map information (tell you how you how to connect pins to outside component, e.g., ultrasound sensors and H-bridge)

## Slide 6: Find correct Pins (important)
#-------------------------------------------------------------
#reuse above pins for New Ultrasound 1
#-------------------------------------------------------------
#set_location_assignment PIN_T14 -to GPIO_1[2]
#set_instance_assignment -name IO_STANDARD "3.3-V LVTTL" -to GPIO_1[2]
#set_location_assignment PIN_T13 -to GPIO_1[3]
#set_instance_assignment -name IO_STANDARD "3.3-V LVTTL" -to GPIO_1[3]
set_location_assignment PIN_T14 -to New_Ultrasound1_rx
set_instance_assignment -name IO_STANDARD "3.3-V LVTTL“ -to New_Ultrasound1_rx
set_location_assignment PIN_T13 -to New_Ultrasound1_tx
set_instance_assignment -name IO_STANDARD "3.3-V LVTTL" –to New_Ultrasound1_tx
GPIO_1[2] -> GPIO12
GPIO_1[3] -> GPIO13
Physical Pins
On Nano

## Slide 7
Software Interface

## Slide 8: Sensors and actuator Interface
Ultrasound sensor interface
uart0.c, uart0.h,
new_ultrasound.c,new_ultrasound.h
Communication interface between Imx6 and Nano
uartcom.c, uartcom.h
(115200 braud rate, 8 data bits, 1 stop bit, Non-parity )
Encoder
please refer to the previous slides
H-bridge interface
please refer to the previous slides

## Slide 9: APIs for Ultrasound
void Ultrasound_init(long Address)
Augments:
Address: used to indicate different ultrasound interface
Find in system.h
unsigned int Ultrasound_read(long Address, unsigned char settings)
Argument:
Address: used to indicate different ultrasound interface
Settings : set the maximum range of measurement (5m or 11m)

## Slide 10: Examples Code -Ultrasound
#include "system.h"
#include "io.h"
#include "stdio.h"
#include "uart0.h“
#include "new_ultrasound.h"
int main()
{
unsigned int res;
unsigned int i;
Ultrasound_init(NEW_ULTRASOUND1_BASE);
while(1)
{
res=Ultrasound_read(NEW_ULTRASOUND1_BASE,0);
printf("The distance is %f m.\n",res*340/1000000.0);
for(i=0;i<100000;i++);
}
return 0;
}

## Slide 11: Connections
Mode Pin is connected to GND to select

## Slide 12
Communication between imx6 and nano

## Slide 13: Simple Communication Protocol (open)
Master-Slave Communication
imx6 (master) send request to nano (slave), while nano (slave) response the request and return data to imx6 (master) .
Synchronization Principle
Use shake hands message to Synchronize master and slave
Master Message Format
Message header (1st byte): 0xaa
Sensor type (2nd byte ): read or write (1bit), sensor type(3 bits), sensor ID(4 bits)
write data (3rd and 4th bytes): data for write command (for H-bridge)
Message Ender: (5th byte): 0x55
Slave Message Format (shake hands message)
Message header: Two byte Data: Message Ender

## Slide 14: APIs
unsigned char message_frame[InFrameByteNum];
Received message frame from imx6 (master)
void Uartcom_init();
Configuration the interrupt and uart
Uartcom_send_frame(unsigned char *data, unsigned char size)
send the shake hand message

## Slide 15: Connections
Imx6 RS232 port<-> Max232 converters <-> Nano
Note: there are two 232 port in Imx6 board. Do not use the debug port.

## Slide 16
Demo Show

## Slide 17: Questions